## Slide 1: Machine Learning Based Real-Time Geosteering
Ngoc Tran
May 06th 2018
Data Analytics Final Project

## Slide 2: Introduction & Problems
14000 horizontal well drilled in 2018 targeted shale plays
However, a few shale plays have multiple target zone.
Real-time geosteering applications: remain in-zone or steer towards a target
Knowledge of petrophysical/ rock mechanical properties surrounding drilling bit
LWD -> information with considerable addition costs
Can we use Drilling measurements to interpret rock properties ?
Machine Learning Techniques to predict lithology by using MWD data

## Slide 3: Data Acquisition
Dataset released by Equinor and taken from Volve field in Norwegian Continental Shelf
12 wells (open hole and MWD logs) and 3 cored wells
  Open Hole logs: neutron, density, GR, sonic and PE logs
  MWD: surface RPM, WOB, Torque, ROP, Downhole Pressure and Temperature, Mud Pump Flow Rate, ECD, etc.

## Slide 4: Workflow
Identify Lithology Clusters on DT, GR and RHOB
15 wells
K-means and Self-Organizing Map (SOM)
Log Data – Sonic (DT), Gamma Ray (GR), Density (RHOB), MWD
Basic statistic analysis: Boxplots and Linear Regression
Petrophysical Significance of Lithology clusters
Identify cluster properties using core data (3 wells)
Predict Lithology clusters using MWD data
Outlier removal (Z-score), Scaling and Centering on 12 wells
KNN, Support Vector Machine and Random Forest

## Slide 5: Basic Statistics Analysis - Lithology
Box plots for log variables in 15 wells:
  GR
  Compressional P-wave slowness (DT)
  Bulk Density (RHOB)
Similar distribution
Notes: Box plots and probability density function (PDF) plots are often best used tools for univariate analysis. Figure 6 shows the box plots for the log variables namely gamma ray (GR), compressional p-wave slowness (DT) and bulk density (RHOB). The figure shows very similar distribution for different wells.

## Slide 6: Basic Statistics Analysis – MWD data
ROP and WOB shows similar distribution
Torque, Pressure, ECD reveals different distribution -> Different depths of zone of interest -> Depth-dependent variables

## Slide 7: Linear Regression: DT vs. NPHI
Linear regression plots
Residual plot
Notes: DT and NPHI good correl, positive correlation. We don’t need to take both logs for cluster and choose 1. NPHI strong impacted by fluid content -> DT is better. B/c wanna choose log sensitive to lithology

## Slide 8: Linear Regression on Torque vs. Temperature
Linear regression plots
Residual plot
Notes: R-square btw Torque and temperature shows the correlation low. R2 even lower among other drilling parameters. Implies different parameters are not correlated to each other.
Residual plot show heteroscedascticity

## Slide 9: K-Means Clustering on Log Data
Notes: Facies 2: shale
Facies 1: calcareous sandstone
Facies 0: shaly sandstone

## Slide 10: Self Organizing Map (SOM) for 3 clusters
Node Grid with GR
Node Grid with DT
Node Grid with RHOB
Facies 2
Facies 2
Facies 2
Facies 1
Facies 1
Facies 1
Facies 0
Facies 0
Facies 0
Notes: Facies 2: GR high, DT high, RHOB low
Facies 1: GR low, DT low, RHOB high
Facies 0: GR intermediate (higher facies 1), DT relatively intermediate and RHOB high

## Slide 11: KNeighbors Classification
This technique predicts facies cluster based on MWD
  Features: MWD Data
  Target: Facies
  Number of Samples: 51877 & Number of features: 6
Using train_test_split package given by Python
  Train set: 80% Dataset & Test set: 20 % Dataset
Hyperparameter Optimization by using GridSearch and Cross Validation KFold

## Slide 12: Support Vector Machine (SVM) classification
This technique predicts facies cluster based on MWD
  Features: MWD Data
  Target: Facies
Using train_test_split package given by Python
  Train set: 80% Dataset & Test set: 20 % Dataset
  Dataset removed outlier (Z-score) and scaled
SVM Model Parameter: C= 10, kernel= Radial Basis Function (rbf)
Confusion Matrix
Scores

## Slide 13: Support Vector Machine (SVM) classification
Facies
Facies
Notes: SVM
Slide shows crossplots among drilling parameters and how measurements for different facies shown up in crossplot.
The three facies 1 has high downP and high ECD
Facies0: low down P and ECD
Facies2: all around
Cross plot DownP and Torque
Facies 1: middle, facies 0: lower and facies 2: distribute throughout

## Slide 14: Random Forest
Using train_test_split package given by Python
  Train set: 80% Dataset & Test set: 20 % Dataset
  Dataset outlier removed (Z-score) and scaled
This method also allows to evaluate the variable importance
Initial tuning parameter: n_estimators= 200, max_depth =5, max_features=4
As for initial tuning parameter
  Memorization performance: 0.882
  Generalization performance: 0.884
Notes: Downhole pressure most important parameter

## Slide 15: Random Forest Hyperparameter Optimization and Validation on Log
Hyperparameter optimization with GridSearch and KFold cross validation

## Slide 16: Conclusions
The unsupervised and supervised techniques shows the great promise
Unsupervised methods allow the predictions of 3 facies
Supervised methods
  KNN gives 94% accuracy in cluster prediction on test dataset
  SVM gives 94% accuracy in cluster prediction on test dataset
  Random Forest gives 93% accuracy in cluster prediction on test dataset
Application to drilling automation and advisory systems
  Prevent out-of-zone drilling
  Minimizes rig-time and equipment
  Cost saving

## Slide 17: References
The dataset for the current study has been taken from the Volve field on the Norwegian Continental Shelf (NCS) released by Equinor ASA. Weblink: https://data.equinor.com/authenticate. [70,000 samples. 21 features]